## Slide 1: Submitted to : Dr. Shaheena Sultana Submitted by : Shazidul Alam Id: 0692220005101009 Batch : CSE-19
8259 Interrupt Controller

## Slide 2: Contents of this template
1. Introduction
2. Features of 8259
3. Pin Configuration of 8259
4. Architecture of 8259
5. Interfacing 8259 with 8086
6. Application Example: Keyboard Interface with 8086 and 8259
7. Conclusion

## Slide 3: Introduction
a) Interrupt - A signal generated by hardware or software to request the processor's attention. b) Need for an Interrupt Controller - Manages multiple interrupt sources, prioritizing them, and directing the processor to the appropriate interrupt service routine (ISR). c) 8259 - Introduced by Intel, widely used in 8085/8086 systems.

## Slide 4: Features of 8259
1. Eight Programmable Interrupt Request Lines (IR0-IR7)
2. Programmable Interrupt Priorities
3. Cascading Capability (up to 8 8259s for 64 interrupts)
4. Automatic EOI (End of Interrupt) Mode
5. Specific EOI Mode
6. Non-Specific EOI Mode
7. Fully Nested Interrupts
8. Buffered Interrupt Requests
9. Programmable Interrupt Masking

## Slide 5: Introduction
Power Supply Pins: Vcc, GND
Interrupt Request Lines: IR0-IR7
Interrupt Request Line: INT
Interrupt Acknowledge Line: INTA
Chip Select Line: CS
Read/Write Line: RD/WR
Data Bus: D0-D7
Cascade Input/Output Lines: CAS0, CAS1, CAS2

## Slide 6: Architecture of 8259
Interrupt Request Register (IRR): Stores pending interrupt requests
In-Service Register (ISR): Stores currently being serviced interrupts
Interrupt Mask Register (IMR): Masks or unmasks interrupt requests
Priority Resolver: Determines the highest priority interrupt request

## Slide 7: Interfacing 8259 with 8086
Initialization:
Program the 8259 using ICW1-ICW4
Set up interrupt vectors in the 8086's interrupt vector table
Interrupt Request:
A peripheral device asserts an interrupt request on one of the IR lines
8259 generates an INT signal to the 8086
Interrupt Acknowledge:
8086 sends an INTA signal to the 8259
8259 sends the interrupt vector number to the 8086
Interrupt Service Routine (ISR):
8086 executes the ISR corresponding to the interrupt vector
ISR should end with an IRET instruction to return control to the interrupted program

## Slide 8: Application Example: Keyboard Interface with 8086 and 8259

## Slide 9: Application Example: Keyboard Interface with 8086 and 8259
Hardware Setup:
Connect keyboard matrix to 8255
Connect 8255 to 8086
Connect 8259 to 8086
Software Implementation:
Initialize 8255 and 8259
Poll keyboard matrix for keypresses
Generate interrupt on keypress
ISR reads keycode and processes it

## Slide 10: An Example Project
Keyboard Interrupt
a) Each ISR should acknowledge the interrupt
b) Service the interrupt (e.g., read keyboard input, update timer, process serial data)
c) Return from interrupt
; ... (Initialization code for 8259)
; Keyboard Interrupt Service Routine
KEYBOARD_ISR:
; Read keyboard input
IN AL, DX ; Read keyboard data from input port
; Process the keypress
; (e.g., display character on screen, store in buffer)
; Acknowledge the interrupt
MOV AL, 20H
OUT 20H, AL
IRET

## Slide 11: Conclusion
8259 is a versatile interrupt controller
It simplifies interrupt handling in 8086-based systems
It can be used in various applications, such as keyboard interfacing, timer-based tasks, and device communication

## Slide 12: Thanks